## Slide 1: Network Layer
Network Layer Characteristics
IPv4 addressing
IPv6 addressing
Sub netting
Routing Protocols

## Slide 2: Network Layer (3rd OSI Layer)
Concerned with getting packets from source to destination.
The network layer must know the topology of the subnet and choose appropriate paths through it.
It is responsible for the source-to-destination delivery of a packet, possibly across multiple networks.

## Slide 3: Network Layer (3rd OSI Layer)
the data link layer oversees the delivery of the packet between two systems on the same network, the network layer ensures that each packet gets from its point of origin to its final destination.
If two systems are connected to the same local network, there is usually no need for a network layer.

## Slide 4: Contd.

## Slide 5: Network Layer Functionalities
Logical addressing
  The physical addressing implemented by the data link layer handles the addressing problem locally.
  If a packet passes the network boundary, we need another addressing system to help distinguish the source and destination systems.
  The network layer adds a header to the packet coming from the upper layer that, among other things, includes the logical addresses of the sender and receiver.

## Slide 6: Contd.
Routing
  When independent networks or links are connected to create internetworks (network of networks) or a large network, the connecting devices (called routers or switches) route or switch the packets to their final destination.
  One of the functions of the network layer is to provide this mechanism.

## Slide 7: Contd.
Internetworking
  Internetworks are multiple networks that are connected in such a way that they act as one large network, connecting multiple office or department networks.
  Internetworks are connected by networking hardware such as routers, switches, and bridges.
  Internetworking is a solution born of three networking problems:
        Isolated LANs
        duplication of resources
        the lack of a centralized network management system.

## Slide 9: Internet Protocol (IP)
used for communicating data across a packet-switched internetwork using the IP Suite, also referred to as TCP/IP.
IP is the primary protocol in the Internet Layer of the Internet Protocol Suite
IP has the task of delivering distinguished protocol datagrams (packets) from the source host to the destination host solely based on their addresses.

## Slide 10: Internet Protocol (IP)
IP defines addressing methods and structures for datagram encapsulation.
The first major version of addressing structure, now referred to as Internet Protocol Version 4 (IPv4) is still the dominant protocol of the Internet
although the successor, Internet Protocol Version 6 (IPv6), is being deployed actively worldwide (128 bits).

## Slide 11: Contd.
Communication at the network layer is host-to-host (computer-to-computer);
  a computer somewhere in the world needs to communicate with another computer somewhere else in the world. Usually, computers communicate through the Internet.

## Slide 12: Contd.
The packet transmitted by the sending computer may pass through several LANs or WANs before reaching the destination computer.
For this level of communication, we need a global addressing scheme; we use the term IP address to mean a logical address in the network layer of the TCP/IP protocol suite.

## Slide 13: IPv4 Addresses
An IPv4 address is a 32-bit address
IPv4 addresses are unique and universal.
They are unique in the sense that each address defines one, and only one, connection to the Internet.
Two devices on the Internet can never have the same address at the same time.

## Slide 14: Address Space
An address space is the total number of addresses used by the protocol.
If a protocol uses N bits to define an address, the address space is 2N because each bit can have two different values (0 or 1) and N bits can have 2N values.

## Slide 15: Address Space
IPv4 uses 32-bit addresses, i.e. the address space is 232 or 4,294,967,296 (more than 4 billion).
if there were no restrictions, more than 4 billion devices could be connected to the Internet.
the actual number is much less because of the restrictions imposed on the addresses.

## Slide 16: Notations
There are two prevalent notations to show an IPv4 address: binary notation and dotted-decimal notation.
Binary Notation
  In binary notation, the IPv4 address is displayed as 32 bits.
  Each octet is often referred to as a byte.
  a 4-byte address.
  an example of an IPv4 address in binary notation:
  01110101 10010101 00011101 00000010

## Slide 17: Notations
Dotted-Decimal Notation
  To make the IPv4 address more compact and easier to read, Internet addresses are usually written in decimal form with a decimal point (dot) separating the bytes.
  The following is the dotted-decimal notation of the above address:
  117.149.29.2

## Slide 18: Notations: Example

## Slide 19: Example 1
Change the following IPv4 addresses from binary notation to dotted-decimal notation
Solution
replace each group of 8 bits with its equivalent decimal number and add dots for separation.

## Slide 20: Example 2
Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Solution
Replace each decimal number with its binary equivalent.

## Slide 21: Example 3
Find the error, if any, in the following IPv4 addresses.
Solution
  There must be no leading zero (045).
  There can be no more than four numbers.
  Each number needs to be less than or equal to 255.
  A mixture of binary notation and dotted-decimal notation is not allowed.

## Slide 22: Class full and Classless addressing
Class full addressing is an IP address allocation method that allocates IP addresses according to five major classes(A-E).
Classless addressing is an IP address allocation method that is designed to replace classful addressing to minimize the rapid exhaustion of IP addresses.

## Slide 23: Class full Addressing
IPv4 addressing, at its inception, used the concept of classes.
This architecture is called class full addressing.
In class full addressing, the address space is divided into five classes: A, B, C, D, and E.
Each class occupies some part of the address space.

## Slide 24: Classful Addressing

## Slide 26
Public IP address | Private IP address
External (global) reach | Internal (local) reach
Used for communicating outside your private network, over the internet | Used for communicating within your private network, with other devices in your home or office
A unique numeric code never reused by other devices | A non-unique numeric code that may be reused by other devices in other private networks
Assigned and controlled by your internet service provider | Assigned to your specific device within a private network
Not free | Free
Any number not included in the reserved private IP address range Example: 8.8.8.8. | 10.0.0.0 — 10.255.255.255; 172.16.0.0 — 172.31.255.255; 192.168.0.0 — 192.168.255.255 Example: 10.11.12.13

## Slide 27: Example 4
Find the class of each address.
  a. 00000001 00001011 00001011 11101111
  b. 11000001 10000011 00011011 11111111
  c. 14.23.120.8
  d. 252.5.15.111
Solution
  a. The first bit is 0. This is a class A address.
  b. The first 2 bits are 1; the third bit is 0. This is a class C address.
  c. The first byte is 14; the class is A.
  d. The first byte is 252; the class is E.

## Slide 28: Classes and Blocks
One problem with class full addressing is that each class is divided into a fixed number of blocks with each block having a fixed size
Number of Blocks for class A = 27
Number of Blocks for class B = 214
Number of Blocks for class C = 221
Block size for class A = 224
Block size for class B = 216
Block size for class C = 28
Notes: 2

## Slide 29: Cont’d
0 [Zero] is reserved and represents all IP addresses.
127 is a reserved address and is used for testing, like a loop back on an interface.
255 is a reserved address and is used for broadcasting purposes.

## Slide 30: Network ID and Host ID

## Slide 31: Mask

## Slide 32: Mask
The mask can help us to find the network ID and the host ID.

## Slide 33: Mask

## Slide 34: Address Depletion
The flaws in class full addressing scheme combined with the fast growth of the Internet led to the near depletion of the available addresses.
Yet the number of devices on the Internet is much less than the 232 address space. We have run out of class A and B addresses, and a class C block is too small for most midsize organizations.
One solution that has alleviated the problem is the idea of classless addressing.

## Slide 35: Classless Addressing
To overcome address depletion and give more organizations access to the Internet, classless addressing was designed and implemented.
In this scheme, there are no classes, but the addresses are still granted in blocks.

## Slide 36: Contd.
A block in class A address is too large for almost any organization. This means most of the addresses in class A were wasted and were not used.
A block in class B is also very large, probably too large for many of the organizations that received a class B block.
A block in class C is probably too small for many organizations.

## Slide 37: Classless Addressing
Address Blocks
  The size of the block (the number of addresses) varies based on the nature and size of the entity.
  For example,
    a household may be given only two addresses;
    a large organization may be given thousands of addresses.
    An ISP, as the Internet service provider, may be given thousands or hundreds of thousands based on the number of customers it may serve.

## Slide 38: Restriction
To simplify the handling of addresses, the Internet authorities impose three restrictions on classless address blocks:
  The addresses in a block must be contiguous, one after another.
  The number of addresses in a block must be a power of 2 (1, 2, 4, 8 .... ).
  The first address must be evenly divisible by the number of addresses.

## Slide 39: Restriction

## Slide 40: Contd.
The above figure shows a block of addresses, in both binary and dotted-decimal notation, granted to a small business that needs 16 addresses.
We can see that the restrictions are applied to this block.
  The addresses are contiguous.
  The number of addresses is a power of 2 (16 = 24)
  the first address is divisible by 16. The first address, when converted to a decimal number, is 3,440,387,360, which when divided by 16 results in 215,024,210.

## Slide 41: Classless addressing Mask
A better way to define a block of addresses is to select any address in the block and the mask.
As we discussed before, a mask is a 32-bit number in which the n leftmost bits are 1s and the 32 - n rightmost bits are 0s.
in classless addressing the mask for a block can take any value from 0 to 32. It is very convenient to give just the value of n preceded by a slash (CIDR – Classless Inter Domain Routing notation).

## Slide 42: Classless addressing Mask
The address and the /n notation completely define the whole block (the first address, the last address, and the number of addresses).
In 1Pv4addressing,a block of addresses can be defined as x.y.z.t/n in which x.y.z.t defines one of the addresses and the /n defines the mask.

## Slide 43: Classless addressing Mask
First Address:
  The first address in the block can be found by setting the 32-n right most bits in the binary notation of the address to Os.
The last address in the block
  can be found by setting the 32 - n rightmost bits in the binary notation of the address to 1s.
The number of addresses in the block
  is the difference between the last and first address.
  It can easily be found using the formula 232-n.

## Slide 44: 2 Power Table
21 | 2
22 | 4
23 | 8
24 | 16
25 | 32
26 | 64
27 | 128
28 | 256
29 | 512
210 | 1024
211 | 2048
212 | 4096
213 | 8192
214 | 16384

## Slide 45: Example 5:
A block of addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28.
  What is the first address in the block?
  What is the last address in the block?
  The number of addresses in the block in the block?

## Slide 46: Solution-Option 1
First Address
  The binary representation of the given address is : 11001101 00010000 00100101 00100111
  If we set 32−28 rightmost bits to 0, we get :
  11001101 00010000 00100101 00100000
Or 205.16.37.32.

## Slide 47: Solution-Option 1
Last Address :
  The binary representation of the given address is
11001101 00010000 00100101 00100111
  If we set 32 − 28 rightmost bits to 1, we get
11001101 00010000 00100101 00101111
or
205.16.37.47

## Slide 48: Solution-Option 1
Number of Addresses :
  The value of n is 28
  Number of addresses is 2 32−28 or 16.

## Slide 49: Option Two
Another way to find the first address, the last address, and the number of addresses is to represent the mask as a 32-bit binary (or 8-digit hexadecimal) number.
This is particularly useful when we are writing a program to find these pieces of information. In the above example the /28 can be represented as
11111111 11111111 11111111 11110000
(twenty-eight 1s and four 0s).

## Slide 50: Cont’d
  Address : 11001101 00010000 00100101 00100111
  Mask : 11111111 11111111 11111111 11110000
Find
  a. The first address
  b. The last address
  c. The number of addresses.

## Slide 51: Solution-Option 2
A. the first address :
  The first address can be found by ANDing the given addresses with the mask.
  ANDing here is done bit by bit.

## Slide 52: Solution-Option 2
B. The last address:
  can be found by ORing the given addresses with the complement of the mask.

## Slide 53: Solution-Option 2
C. The number of addresses:
  can be found by complementing the mask, interpreting it as a decimal number, and adding 1 to it.

## Slide 54: Subnetting
During the era of class full addressing, subnetting was introduced.
If an organization was granted a large block in class A or B, it could divide the addresses into several contiguous groups and assign each group to smaller networks (called subnets) or, in rare cases, share part of the addresses with neighbors.
Subnetting increases the number of 1s in the mask.

## Slide 55: Attributes of Subnetting
Network ID
Broadcast IP
First host IP
Last host IP
Next network
#IP addresses in each block
CIDR/subnet

## Slide 56: Network Address and Host Address
When an organization is given a block of addresses, the organization is free to allocate the addresses to the devices that need to be connected to the Internet.
It defines the organization itself to the rest of the world.
The first address is the one that is used by routers to direct the message sent to the organization from the outside.

## Slide 57: Network Address and Host Address
The Network address identifies the specific network to which host is attached, and Host address uniquely identifies a host within a network.
The distinction is important because router routes the packet according to a network address and don't care about host address.

## Slide 58: Subnetting Types
FLSM (Fixed Length Subnet Masks) Subnetting | VLSM (Variable Length Subnet Masks) Subnetting
All subnets are equal in size. | Subnets are variable in size.
All subnets have equal number of hosts. | Subnets have variable number of hosts.
All subnets use same subnet mask. | Subnets use different subnet masks.
It is easy in configuration and administration. | It is complex in configuration and administration.
It wastes a lot of IP addresses. | It wastes minimum IP addresses.
It is also known as classfull Subnetting. | It is also known as classless Subnetting.
It supports both classfull and classless routing protocols. | It supports only classless routing protocols.

## Slide 59
.0 /24 .255
.0 /25 .127
.128 /25 .255
/26
/26
/26
/26
/27
/27
/27
/27
/27
/27
/27
/27
/25
/27
/27
/26

## Slide 60: Subnetting table
Subnet | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
Host | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
CIDR | /24 | /25 | /26 | /27 | /28 | /29 | /30 | /31 | /32
Subnet Mask | 0 | 128 | 192 | 224 | 240 | 248 | 252 | 254 | 255
3rd octate | /16 | /17 | /18 | /19 | /20 | /21 | /22 | /23 | /24
Example:
Given: 192.168.4.0/24
Required : 3 subnets

## Slide 61: Cont’d
Solution

## Slide 62: Exercise find all subnet attributes
10.1.1.55/28
Network ID: | 10.1.1.48
Broadcast IP: | 10.1.1.63
First host IP : | 10.1.1.49
Last host IP : | 10.1.1.62
Next network : | 10.1.1.64
#IP addresses in each block : | 16
CIDR/subnet | /28 250.250.240.0

## Slide 63: Exercise find all subnet attributes
10.1.1.37/29
Network ID: | 10.1.1.32
Broadcast IP: | 10.1.1.39
First host IP : | 10.1.1.33
Last host IP : | 10.1.1.38
Next network : | 10.1.1.40
#IP addresses in each block : | 8
CIDR/subnet | /29 255.255.255.248

## Slide 64: Exercise find all subnet attributes
10.2.2.20/30
Network ID: | 10.2.2.20
Broadcast IP: | 10.2.2.23
First host IP : | 10.2.2.21
Last host IP : | 10.2.2.22
Next network : | 110.2.2.24
#IP addresses in each block : | 4
CIDR/subnet | /27 255.255.255.252

## Slide 65: Exercise find all subnet attributes
10.2.2.199/26
10.2.2.0 10.2.2.64 10.2.2.128 10.2.2.192 10.2.3.0 10.2.3.64 . . .

## Slide 66: Exercise find all subnet attributes
10.2.2.199/26
Network ID: | 10.2.2.192
Broadcast IP: | 10.2.2.255
First host IP : | 10.2.2.193
Last host IP : | 10.2.2.254
Next network : | 10.2.3.0
#IP addresses in each block : | 64
CIDR/subnet | /26 255.255.255.192

## Slide 67: Example
20 hosts
40 hosts
10 hosts
100 hosts
192.168.1.0

## Slide 68: VLSM:100 hosts
2h-2>=100
  h=7
\value
  8+8+8+(8-7)=25
Subnet mask
  11111111.11111111.11111111.10000000
  255.255.255.128
Block size
  27=128
  Range: 192.168.1.0/25 -192.168.1.127/25

## Slide 69: VLSM: 40 hosts
2h-2>=40
  h=6
\value
  8+8+8+(8-6)=26
Subnet mask
  11111111.11111111.11111111.11000000
  255.255.255.192
Block size
  26=64
  Range: 192.168.1.128/26 -192.168.1.191/26

## Slide 70: VLSM : 20 hosts
2h-2>=20
  H=5
\value
  8+8+8+(8-5)=27
Subnet mask
  11111111.11111111.11111111.11100000
  255.255.255.224
Block size
  25=32
  Range: 192.168.1.192/27 -192.168.1.223/27

## Slide 71: VLSM: 10 hosts
2h-2>=10
  H=4
\value
  8+8+8+(8-4)=28
Subnet mask
  11111111.11111111.11111111.11110000
  255.255.255.240
Block size
  24=16
  Range: 192.168.1.224/28 -192.168.1.239/28

## Slide 72: VLSM
  192.168.1.0/25 -192.168.1.127/25 for 100 hosts
  192.168.1.128/26 -192.168.1.191/26 for 40 hosts
  192.168.1.192/27 -192.168.1.223/27 for 20 hosts
  192.168.1.224/28 -192.168.1.239/28 for 10 hosts

## Slide 73: Example 6: Problem
Suppose an organization is given the block 17.12.14.0/26, which contains 64 addresses. The organization has three offices and needs to divide the addresses into three sub blocks of 32, 16, and 16 addresses.

## Slide 74: Example 6: Solution
  Suppose the mask for the first subnet is n1, then 232-n1 must be 32, which means that n1 = 27.
  Suppose the mask for the second subnet is n2, then 232-n2 must be 16, which means that n2 = 28.
  Suppose the mask for the third subnet is n3, then 232-n3 must be 16, which means that n3 = 28.
This means that we have the masks 27, 28, 28 with the organization mask being 26.

## Slide 76: Address Allocation
The next issue in classless addressing is address allocation.
How are the blocks allocated?
The ultimate responsibility of address allocation is given to a global authority called the Internet Corporation for Assigned Names and Addresses (ICANN).
However, ICANN does not normally allocate addresses to individual organizations. It assigns a large block of addresses to an ISP.

## Slide 77: Address Allocation
Each ISP, in turn, divides its assigned block into smaller sub blocks and grants the sub blocks to its customers.
In other words, an ISP receives one large block to be distributed to its Internet users. This is called address aggregation.
many blocks of addresses are aggregated in one block and granted to one ISP.

## Slide 78: Example 7
An ISP is granted a block of addresses starting with 190.100.0.0/16 (65,536 addresses).
The ISP needs to distribute these addresses to three groups of customers as follows:
  a. The 1st group has 64 customers; each needs 256 addresses.
  b. The 2nd group has 128 customers; each needs 128 addresses.
  c. The 3rd group has 128 customers; each needs 64 addresses.
Design the sub blocks and find out how many addresses are still available after these allocations.

## Slide 79: solution
Group 1
For this group, each customer needs 256 addresses.
This means that 8 bits are needed to define each host.
The prefix length is then 32 − 8 = 24. The addresses are

## Slide 80: solution
Group 2
For this group, each customer needs 128 addresses.
This means that 7 bits are needed to define each host.
The prefix length is then 32 − 7 = 25. The addresses are

## Slide 81: Solution
Number of granted addresses to the ISP: 65,536
Number of allocated addresses by the ISP: 40,960
Number of available addresses: 24,576
Group 3
For this group, each customer needs 64 addresses. This means that 6 bits are needed to each host.
The prefix length is then 32 − 6 = 26. The addresses are

## Slide 82: Reading Assignment:
How NAT works
What is NAT
Why NAT is important

## Slide 83: IPv6 ADDRESSES
Despite all short-term solutions, address depletion is still a long-term problem for the Internet.
This and other problems in the IP protocol itself have been the motivation for IPv6.
An IPv6 address is 128 bits or 32 hexadecimal digits long.

## Slide 84: Internet Protocol
IPV4 | IPV6
32 bit | 128 bit
4 octate | 8 blocks
Decimal Representation | Hexadecimal Representation
1 ocate -8 bit | 1 block -16bit
4*8 =32bit | 8*16 =128bit
Subnet mask | No subnet mask
5 classes | No class
Use broadcast address | Not use any broadcast
Contain 0-255 devices | Contain 65,536 (FFFF)
Security add on | Embedded Security

## Slide 85: IPv6 ADDRESSES

## Slide 86: Abbreviated IPv6 addresses

## Slide 87: Example 9
Expand the address 0:15::1:12:1213 to its original.
Solution
We first need to align the left side of the double colon to the left of the original pattern and the right side of the double colon to the right of the original pattern to find how many 0s we need to replace the double colon.
This means that the original address is.

## Slide 88: What does a router do?
Find path
Forward packets

## Slide 89: Routing vs Forwarding
Routing :
  Building maps and giving directions
Forwarding:
  Moving packets between interfaces according to the directions

## Slide 90: IP Routing
Path derived from information received from a routing protocol
Several alternative paths may exist
  best path stored in forwarding table
Decisions are updated periodically or as topology changes (event driven)
Decisions are based on:
  topology
  policies and metrics (hop count, filtering, delay, bandwidth, etc.)

## Slide 91: IP Forwarding
Router decides which interface a packet is sent to
Forwarding table populated by routing process
Forwarding decisions:
  destination address
  class of service (fair queuing, precedence, others)
  local requirements (packet filtering)
Forwarding is usually aided by special hardware

## Slide 92: Contd.
The delivery of a packet to its final destination is accomplished by using two different methods of delivery, direct and indirect.
Direct delivery occurs when the source and destination of the packet are located on the same physical network or when the delivery is between the last router and the destination host

## Slide 93: Contd.

## Slide 94: Routing Table
A host/router has routing table with an entry for each destination, or combination of destinations, to route IP packets.
The routing table can be either static or dynamic.
Depending on network requirement we can use :
  Static routing
  Dynamic routing
  a combination of both dynamic and static routing.

## Slide 95: Static Routing Table
Contains information entered manually.
Administrator enters the route for each destination into table.
When a table is created, it cannot update automatically when there is a change in the Internet and the table must be manually altered by the administrator.
Can be used in small internet that doesn’t change very often, or in an experimental internet for troubleshooting.
It is poor strategy to use a static routing table in a big internet such as the Internet.

## Slide 96: Dynamic Routing Table
Updated periodically by using one of the dynamic routing protocols such as RIP, OSPF, or BGP.
Whenever there is a change in the Internet, such as a shutdown of a router or breaking of a link, the dynamic routing protocols update all the tables in the routers (and eventually in the host) automatically.
The routers in a big internet such as the Internet need to be updated dynamically for efficient delivery of the IP packets.

## Slide 97: Routing Table Format
A routing table for classless addressing has a minimum of four columns.
However, some of today's routers have even more columns.
We should be aware that the number of columns is vendor-dependent, and not all columns can be found in all routers.

## Slide 98: Routing Table Format
Mask:- defines the mask applied for the entry.
Network address:- defines network address to which packet is finally delivered.
Next-hop address:- defines address of next-hop to which packet is delivered
Interface:- shows the name of the interface.
Flags:- on/off switches that signify either presence/absence. There 5 flags
  U (up):- indicates the router is up and running
  G (gateway):- means that the destination is in another network
  H (host-specific):- indicates that the entry in the network address field is a host-specific address.
  D (added by redirection):- indicates that routing information for this destination has been added to the host routing table by a redirection message from ICMP.
  M (modified by redirection):- indicates that the routing information for this destination has been modified by a redirection message from ICMP.
Reference count:- gives the number of users of this route at the moment.
Use:- shows the number of packets transmitted through this router

## Slide 99: Routing Protocols
Routing protocols have been created in response to the demand for dynamic routing tables.
A routing protocol is a combination of rules and procedures that lets routers in the internet inform each other of changes.
It allows routers to share whatever they know about the internet or their neighborhood.

## Slide 100: Routing Protocols
Routing protocols insure that packet takes the best path from these paths.
To accomplish this task, a router will need to perform following:
  Learn about the directly connected routers on its interface
  Find the networks that they have
  Build routing table from this information
  Choose best network from routing table to send the packet

## Slide 101: Purpose of Dynamic Routing Protocols
Routing Protocols are used to facilitate the exchange of routing information between routers.
The purpose of dynamic routing protocols includes:
  Discovery of remote networks
  Maintaining up-to-date routing information
  Choosing the best path to destination networks
  Ability to find a new best path if the current path is no longer available

## Slide 102: Routing Updates
Routing update is a mechanism of sharing information with neighboring routers.
In a particular time duration router advertise its routing information through broadcast or multicast.
Different protocols have different time intervals.
Routing updates contain all necessary information for routing protocol such as learned network, timers, AS, AD, matrix values, interface details etc.

## Slide 103: Types of Routing Protocols
Routing Protocols
Intra domain
Distance vector
Link state
Inter domain
Path vector
RIP
OSPF
BGP

## Slide 104: Intra and Inter domain Routing
Today, an internet can be so large that one routing protocol cannot handle task of updating the routing tables of all routers.
For this reason, an internet is divided into autonomous systems (AS)

## Slide 105: Autonomous systems (AS)
  AS is a group of networks and routers under the authority of a single administration.
  AS is a boundary line for routing protocol.
  It could be your company, or group of companies.
  It is defined by a numeric value.
  To distinguish between different AS, Internet Assigned Numbers Authority (IANA) provides a range from 1 to 65535.

## Slide 106: Intra domain vs Inter domain
Routing inside an autonomous system is referred to as intra domain routing (Interior gateway protocols (IGPs))
routing between autonomous systems is referred to as inter domain routing (Exterior gateway protocols (EGPs) ).
Each AS can choose one or more intra domain routing protocols to handle routing inside the AS. However, only one inter domain routing protocol handles routing between autonomous systems

## Slide 107: Intra domain vs Inter domain
Some examples of IGPs are:
  RIPv1
  RIPv2
  EIGRP
  IGRP
  OSPF
Example of EGPs is Border Gateway Protocol (BGP).

## Slide 108: Distance Vector Routing
It uses distance (metric value) and direction (vector) to find the best path to destination network
In distance vector routing, the least-cost route between any two nodes is the route with minimum distance.
In this protocol, as the name implies, each node maintains a vector (table) of minimum distances to every node.
Shortest path

## Slide 109: Distance Vector Routing
The table at each node also guides the packets to the desired node by showing the next stop in the route (next-hop routing).
We can think of nodes as the cities in an area and the lines as the roads connecting them.
A table can show a tourist the minimum distance between cities.

## Slide 110: Cont….

## Slide 111: Link State Routing
Link state routing protocols use more composite metric to locate the best path for destination network.
It maintains three separate tables.
  First table keeps track of directly connected neighbors.
  Second table determines the entire network topology
  the third is the routing table that keeps actual path.
The node can use Dijkstra's algorithm to build a routing table
best path (consider the speed of the link)
OSPF is the example of link state protocol

## Slide 112: Cont….

## Slide 113: Distance vector and Link State
Distance Vector
Routers communicate with neighbor routers advertising networks as measures of distance and vector
Distance =metric , vector=direction(interface)
Knowledge of the network from directly connected neighbors
Send periodic updates of entire routing table
Best for simple, flat design ,non hierarchical networks ,minimum administration knowledge , convergence time is not an issue
Link State
Routers communicate with all other routers exchanging link state information to build a topology or the entire network
Link-state=interface connections or “links” to other routers and networks
Routers have a complete view of the network ,knowledge of the entire topology
Send triggered partial updates
Best for large, hierarchical networks ,advanced administration knowledge ,convergence time is crucial

## Slide 114: Thank You